TRL	Low Frequency High Frequency / R L G C R L G C
Parallel Plate d << b	2 over {%sigma_c %delta b}	{%mu d} over b	{%sigma b} over d	{%epsilon^' b} over d	2 over {%sigma_c %delta b}	{%mu d} over b	{%sigma b} over d	{%epsilon^' b} over d
Coaxial	1 over {%pi %sigma_c} left( 1 over a^2 + 1 over {c^2 - b^2} right)	%mu over {2 %pi} left[ ln b over a + 1 over 4 + 1 over {4 (c^2 - b^2)} left( b^2 - 3c^2 + {4c^2} over {c^2 - b^2} ln c over b right) right]	{2 %pi %sigma} over {ln left(b / a right)}	{2 %pi %epsilon^'} over {ln left(b / a right)}	1 over {2 %pi %sigma_c %delta} left( 1 over a + 1 over b right)	%mu over {2%pi} {ln left(b over a right)}	{2 %pi %sigma} over {ln left(b / a right)}	{2 %pi %epsilon^'} over {ln left(b / a right)}
Two wire	2 over {%pi a^2 %sigma_c}	%mu over %pi left[1 over 4 +cosh^-1 left( d over {2a} right) right]	{%pi %sigma} over {cosh^-1 left(d over {2a}right)}	{%pi %epsilon^'} over {cosh^-1 left(d over {2a}right)}	1 over {%pi a %delta %sigma_c}	%mu over %pi cosh^-1 left( d over {2a} right)	{%pi %sigma} over {cosh^-1 left(d over {2a}right)}	{%pi %epsilon^'} over {cosh^-1 left(d over {2a}right)}
Microstrip line	C_0= left lbrace binom {{2%pi%epsilon_0} over {ln left( {8d} over w + w over {4d} right)} ; {w over d}<=1} {%epsilon_0 left[ w over d +1.393 + 0.667 {ln left( w over d + 1.4444 right)} right]; {w over d}>1} right none / %epsilon_{r_eff}= {%epsilon^'_r+1} over 2 + {%epsilon^'_r-1} over 2 left( 1+ {12d} over w right)^-{1 over 2} + left lbrace binom {0.002 (%epsilon^'_r - 1) left( 1- w over d right)^2 ;w over d<1} {0; w over d>1} right none / Z_0 = sqrt{ {%mu_0 %epsilon_0} over %epsilon_{r_eff}} 1 over C_0				No closed form