	Wave in Low loss Dielectric	Wave in Low Loss Transmission line
Velocity	v_p = {1} over {sqrt{%mu%epsilon}}	v_p = {1} over {sqrt{LC}}
Wavenumber	%beta = {2 %pi} over {%lambda}	%beta = {2 %pi} over {%lambda}
Impedance	%eta = sqrt{{j %omega %mu} over {%sigma + j %omega %epsilon^'}} approx sqrt{{%mu} over {%epsilon}}	Z_0 = sqrt{{R+j %omega L} over {G + j %omega C}} approx sqrt{{L} over {C}}
Loss Tangent	tan(%theta) = %sigma over {%omega%epsilon^{'}}	tan(%theta) = G over {%omega C}
attenuation	%alpha approx {1 over 2} left(%sigma sqrt{%mu over %epsilon^'}right)	%alpha approx {1 over 2} left( R sqrt{C over L} + G sqrt{L over C}right)
Phase constant	%beta approx %omega sqrt{%mu%epsilon^'} left[ 1+ {1 over 8} left( {%sigma over {%omega %epsilon^'}} right)^2 right]	%beta approx %omega sqrt{LC} left[ 1+ {1 over 8} left( {R over {%omega L}}-{G over {%omega C}} right)^2 right]

	Wave in Good Conductor %sigma over {%omega %epsilon^'}>>1	Wave in Low loss Dielectric %sigma over {%omega %epsilon^'}<<1
Velocity	v_p = %omega%delta	v_p = {1} over {sqrt{%mu%epsilon}}
Wavenumber	%beta = {2 %pi} over {%lambda}	%beta = {2 %pi} over {%lambda}
Impedance	%eta = {1+j} over {%sigma %delta}	%eta = sqrt{{%mu} over {%epsilon}}
Loss	R = 1 over {2a%sigma %pi %delta} left(%OMEGA/m right)	tan(%theta) = %sigma over {%omega%epsilon^{'}}
attenuation	%alpha approx sqrt{%pi f %mu %sigma}	%alpha approx {1 over 2} left(%sigma sqrt{%mu over %epsilon^'}right)
Phase constant	%beta approx sqrt{%pi f %mu %sigma}	%beta approx %omega sqrt{%mu%epsilon^'} left[ 1+ {1 over 8} left( {%sigma over {%omega %epsilon^'}} right)^2 right]
Skin depth	%delta = 1 over sqrt{%pi f %mu %sigma}	-

General case: %alpha = %omega sqrt{{%mu %epsilon^'} over 2} sqrt{sqrt{1+left ( %epsilon^{''} over %epsilon^{'} right )^2} -1} %beta = %omega sqrt{{%mu %epsilon^'} over 2} sqrt{sqrt{1+left ( %epsilon^{''} over %epsilon^{'} right )^2} +1}
	Uniform Plane Wave	Transmission line
Reflection coefficient	%GAMMA = {%eta_2-%eta_1} over {%eta_2+%eta_1}	%GAMMA = {Z_2-Z_1} over {Z_2+Z_1}
Transmission coefficient	%tau = 1+%GAMMA = {2%eta_2} over {%eta_2+%eta_1}	%tau = 1+%GAMMA = {2 Z_2} over {Z_2+Z_1}
Reflected Power Ratio	{langle S_1r rangle} over {langle S_1i rangle} = lline %GAMMA rline^2	{langle S_1r rangle} over {langle S_1i rangle} = lline %GAMMA rline^2
Transmitted power ratio	{langle S_2t rangle} over {langle S_1i rangle} = 1- lline %GAMMA rline^2	{langle S_2t rangle} over {langle S_1i rangle} = 1- lline %GAMMA rline^2
Standing wave ratio	SWR = {1+ lline %GAMMA rline} over {1- lline %GAMMA rline}	SWR = {1+ lline %GAMMA rline} over {1- lline %GAMMA rline}
Impedance transfer	%eta_w = %eta_2 {%eta_3 + j %eta_2 tan(%beta_2 l)} over {%eta_2 + j %eta_3 tan(%beta_2 l)}	Z_i = Z_2 {Z_3 + j Z_2 tan(%beta l)} over {Z_2 + j Z_3 tan(%beta l)}
Quarter-wave matching	%eta_2 = sqrt{%eta_1 %eta_3}	%Z_2 = sqrt{%Z_1 %Z_3}